# Series

ORA-C	C Range Commercial Air Curtain

# Features

Model	-	Electric heat.

-	No heat.

Color	-	Standard: white.

- Custom colors available upon request (RAL Chart).

Voltage	-	208V, 240/208V, 480V, 600V, 60 Hz.

Construction	-	Steel casing with resistant plastic end caps.

-	Quick access to the internal components thanks to the front panel which facilitate maintenance and connection.

-	High-limit temperature control with automatic reset.

Fan	-	Tangential fans.

Heating element	-	Element provides instant heat (electric model).

Control	-	Ecopower control included (20 ft. (6 m) RJ9 control included).

- Door switch included.

- Compatible with a Building Management System.

- Personalize programing of the air curtain.

Installation	-	Maximum height installation:

- Surface-mounted: 9.84 ft. (3 m) above the floor.

- Recessed: 9.84 ft. (3 m) above the floor.

-	Surface-mounted: low profile installation brackets included.

-	Ceiling hanging: fixings are included for 1/4 in. x 20 UNC threaded rods (not supplied).

-	Recessed: hinged core grilles included for easy installation and maintenance.

-	Joining kit, available in option, for connecting multiple surface mounted units.

Warranty	-	2-year warranty against defects.

Application	-	Entrance way, vestibule, commercial building, service door, hospital.

# Models

| Product # | Qty | Volts (ph) | kW Lo/Hi | Amp. | cfm | Max velocity (ft./min) | dBA at 3 m | Effective width of air stream | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | in. | mm | lb | kg |
| Surface-mounted |
| Electric heat |
| C1000ENTECO600V |  | 600 (3) + 208 ou 2401 | 4.5/9 | 9.3 | 740 | 1500 | 55.0 | 33 | 838 | 35 | 16 |
| C1500ENTECO600V |  | 600 (3) + 208 ou 2401 | 6/12 | 12.8 | 1060 | 1500 | 55.0 | 52 | 1320 | 51 | 23 |
| C2000ENTECO600V |  | 600 (3) + 208 ou 2401 | 9/18 | 18.6 | 1470 | 1500 | 56.0 | 66 | 1676 | 73 | 33 |
| C1000ENTECO480V |  | 480 (3) + 208 ou 2401 | 4.5/9 | 10.9 | 740 | 1500 | 55.0 | 33 | 838 | 35 | 16 |
| C1500ENTECO480V |  | 480 (3) + 208 ou 2401 | 6/12 | 14.5 | 1060 | 1500 | 55.0 | 52 | 1320 | 51 | 23 |
| C2000ENTECO480V |  | 480 (3) + 208 ou 2401 | 9/18 | 21.7 | 1470 | 1500 | 56.0 | 66 | 1676 | 73 | 33 |
| C1000ENTECO208V |  | 208 (3) | 4.5/9 | 27 | 740 | 1500 | 55.0 | 33 | 838 | 35 | 16 |
| C1500ENTECO208V |  | 208 (3) | 6/12 | 36 | 1060 | 1500 | 55.0 | 52 | 1320 | 51 | 23 |
| C2000ENTECO208V |  | 208 (3) | 9/18 | 54 | 1470 | 1500 | 56.0 | 66 | 1676 | 73 | 33 |
| No heat |
| C1000ANTECO208-230V |  | 208/240 (1)2 | - | 0.5 | 740 | 1500 | 55.0 | 33 | 838 | 35 | 15 |
| C1500ANTECO208-230V |  | 208/240 (1)2 | - | 0.7 | 1060 | 1500 | 55.0 | 52 | 1320 | 46 | 21 |
| C2000ANTECO208-230V |  | 208/240 (1)2 | - | 1 | 1470 | 1500 | 56.0 | 66 | 1676 | 68 | 31 |
| Recessed |
| Electric heat |
| C1000ERECO600V |  | 600 (3) + 208 ou 2401 | 4.5/9 | 9.3 | 700 | 1500 | 55.0 | 33 | 838 | 40 | 19 |
| C1500ERECO600V |  | 600 (3) + 208 ou 2401 | 6/12 | 12.8 | 1020 | 1500 | 55.0 | 52 | 1320 | 56 | 25 |
| C2000ERECO600V |  | 600 (3) + 208 ou 2401 | 9/18 | 18.6 | 1400 | 1500 | 56.0 | 66 | 1676 | 79 | 35 |
| C1000ERECO480V |  | 480 (3) + 208 ou 2401 | 4.5/9 | 10.9 | 700 | 1500 | 55.0 | 33 | 838 | 40 | 19 |
| C1500ERECO480V |  | 480 (3) + 208 ou 2401 | 6/12 | 14.5 | 1020 | 1500 | 55.0 | 52 | 1320 | 56 | 25 |
| C2000ERECO480V |  | 480 (3) + 208 ou 2401 | 9/18 | 21.7 | 1400 | 1500 | 56.0 | 66 | 1676 | 79 | 35 |
| C1000ERECO208V |  | 208 (3) | 4.5/9 | 27 | 740 | 1500 | 55.0 | 33 | 838 | 44 | 20 |
| C1500ERECO208V |  | 208 (3) | 6/12 | 36 | 1060 | 1500 | 55.0 | 52 | 1320 | 60 | 27 |
| C2000ERECO208V |  | 208 (3) | 9/18 | 54 | 1470 | 1500 | 56.0 | 66 | 1676 | 87 | 37 |
| No heat |
| C1000ARECO208-230V |  | 208/240 (1)2 | - | 0.5 | 740 | 1500 | 55.0 | 33 | 838 | 39 | 19 |
| C1500ARECO208-230V |  | 208/240 (1)2 | - | 0.7 | 1060 | 1500 | 55.0 | 52 | 1320 | 52 | 25 |
| C2000ARECO208-230V |  | 208/240 (1)2 | - | 1 | 1470 | 1500 | 56.0 | 66 | 1676 | 74 | 35 |

To order any custom colors from the R.A.L. chart, add “SP” at the end of the Product # and specify RAL color # on the order. Contact our customer service department for lead times.

1 IMPORTANT: 600V and 480V models need 2 power sources (E.g.: 600V+208V or 230V) or an external transformer (E.g.: 600V/240V). The VA requirement varies between models: C1000 = 200VA, C1500 and C2000 = 350VA.

2 Maximum installation height when connected to 208V is 8.53 ft. (2.6 m).

# Options

| Product # Kit | Description | Qty |
| --- | --- | --- |
| ORA-EEPROM | EEPROM memory |  |
| ORA-RS-485 | Cable RS-485 to USB adaptor |  |
| T7263627 | Programming board |  |
| T5951001 | Master and slave lead: 9.84 ft. (3 m) |  |
| T5951050 | Ecopower extension lead: 32.80 ft. (10 m) |  |
| T5951060 | Ecopower extension lead: 49.21 ft. (15 m) |  |
| T5951020 | Ecopower extension lead: 98.42 ft. (30 m) |  |
| T5951030 | Extention lead coupler |  |

### Others

| Type | Quantity | Model et description Complementary informations | Volts | Phase | Watts | Length mm/in. | Informations Color/installation |
| --- | --- | --- | --- | --- | --- | --- | --- |

# Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| ELectrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |