# Series

OSR	Controller options for pipe tracing for use in non-hazardous (ordinary) locations

|  | Product # | DescrIption | Qty |
| --- | --- | --- | --- |
|  | ECA-E55-R25HT1 | SPDT, NEMA 4X thermostat. Die-cast aluminum housing, epoxy coating with stainless steel powder. 22A at 120/250/480V. 10 ft. (3 m) stainless steel bulb and capillary. Ambient temperature: -40°C to 71°C (-40°F to 160°F). |  |
|  | TPR-L1N-3X-Q101 | SPDT, NEMA 4X thermostat. Polycarbonate housing. 22A at 120/250/480V. 3 ft. (1 m) tinned copper bulb and capillary. Ambient temperature: -34°C to 60°C (-30°F to 140°F). |  |
|  | TPR-L1N-10X-Q101 | SPDT, NEMA 4X thermostat. Polycarbonate housing. 22A at 120/250/480V. 10 ft. (3 m) tinned copper bulb and capillary. Ambient temperature: -34°C to 60°C (-30°F to 140°F). |  |
|  | TRF115-0051 | SPDT, NEMA 4X thermostat. Noryl plastic housing. 25A at 120/208/240/277V. 5 ft. (1.5 m) stainless steel bulb and capillary. Ambient temperature: -17°C to 49°C (0°F to 120°F). |  |
|  | TRF115-0071 | SPDT, NEMA 4X thermostat. Noryl plastic housing. 25A at 120/208/240/277V. 8 ft. (2.4 m) copper bulb and capillary. Ambient temperature: -35°C to 38°C (-30°F to 100°F). |  |
|  | ELTC-14-RTD1 | Digital temperature control. Polycarbonate housing. 20A at 90-260V. 3-wire RTD (Pt-100) sensing element is 5 x 50 mm with 5 m of ﬂuoropolymer lead wires. Ambient temperature: 0°C to 250°C (32°F to 482°F). |  |

1 Requires a ground fault circuit interrupter (GFCI) in the electrical panel.

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |