Series

SRG-PI	120V Preassembled Self-Regulating Heating Cable

Features

Nominal voltage	-	120V.

Cold lead length	-	36’’ (0.9 m).

Outer jacket	-	Thermoplastic.

Bus wire	-	Nickel plated copper.

Maximum operating

temperature (power on)	-	60 °C (140 °F).

Maximum operating

temperature (power off)	-	80 °C (176 °F).

Cable section	-	14.1 mm X 5.6 mm.

Bending radius, minimum	-	25 mm (1 in.).

Included hardware	- Grounded 3-pronged plug with indicator light to show when the cable is on.

Minimum installation and

start-up temperature	-	-25 °C (-13 °F).

Standards	- 	CSA C22.2.130.03; -WS.

- CAN/CSA 60079-7:12, 60079-0-11.

- ANSI/IEEE 515, 515.

Certification	- 	CSA C US 2547790

Rating	-  Wet rated, for outdoor use (WS).

Warranty	-	1-year basic warranty on the heating cable.

Application	-	Freeze protection, roof and gutter, pipes.

Models

| Product #1 | Length | Nominal power output in air condition at 5 °C (40 °F)2 | Qty |
| --- | --- | --- | --- |
|  | ft. | m | Watts |  |
| ECK-7AO-006 | 6 | 1.8 | 42 |  |
| ECK-7AO-012 | 12 | 3.6 | 84 |  |
| ECK-7AO-018 | 18 | 5.5 | 126 |  |
| ECK-7AO-025 | 25 | 7.6 | 175 |  |
| ECK-7AO-050 | 50 | 15.2 | 350 |  |
| ECK-7AO-075 | 75 | 22.9 | 525 |  |
| ECK-7AO-100 | 100 | 30.5 | 700 |  |

1 Must be plugged into a 120V outlet fitted with ground fault protection device (GFCI).

2 Because of the cable's self-regulating properties, the power density can reach up to 11 Watts per foot when buried in snow or ice: "wet density". In this situation, use of a 15 Amp. circuit breaker is valid for all models.

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electricial Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact at manufacturer: |  |
| Comments: |