Series

OVN	Electronic Bathroom Fan Heater

Features

Color	-	Standard: white, almond.

-	Optional (upcharge applicable): metallic silver, bronze, metallic charcoal,

aluminum, semi-gloss black, sand.

- Custom colors available upon request.

Finish	-	Standard: epoxy/polyester powder paint.

Voltage	-	240/208V, 1-phase.

Construction	-	Cast aluminum front cover.

-	Steel bar grilles prevent the insertion of foreign objects; smooth-ﬁnish paint is washable and anti-yellowing.

-	High-limit temperature control with automatic reset.

Fan	-	Whisper-quiet squirrel-cage fan.

-	Factory-lubricated, two-speed motor.

Heating element	-	Nickel-chromium alloy stitched wire protected by mica insulators.

-	Heating element provides instant heat.

Control	-	Built-in electronic digital thermostat/timer with backlit display that can be used as a

night light.

-	Electronic thermostat with 2 triacs automatically switches from 750W to 1500W when needed.

-	Electronic boost heating mode: 1-30 minutes.

-	Standby mode, ideal for cottages.

-	Keypad lock function that eliminates unwanted temperature adjustments and the use of the thermostat modes.

Installation	-	4 in. (102 mm) minimum clearance to ﬂoor.

-	May be recessed or surface-mounted without adaptor in 2 in. X 3 in. stud partitions

with gypsum.

-	Single-screw built-in wire holder and mounting holes for fast and easy installation.

-	Template included.

Warranty	-	5-year warranty against defects.

Application	-	Bathroom, kitchen, living room, entrance way.

Model

| Product # | Qty | Volts | Watts | Weight |
| --- | --- | --- | --- | --- |
|  |  |  | min. | max. | lb | kg |
| OVN1500-TH |  | 240/208 | 750/563 | 1500/1125 | 16.3 | 7.4 |

# Options

| Product # Kit | Product # Factory installed* | Description | Qty |
| --- | --- | --- | --- |
| KIT-OVN-DIS1 | DIS1 | Disconnect switch, 20A at 250V |  |

* For factory installed options, add the option number to the product number. See the Product Code section inside the front cover.

1 For the U.S. only: The nominal current of the unit must not exceed 80% of the capacity of the disconnect.

Add"BL" for white, "AM" for almond.

### Others

| Type | Quantity | Model et description Complementary information | Volts | Phase | Watts | Length mm/in. | Information Color/installation |
| --- | --- | --- | --- | --- | --- | --- | --- |

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |