Low Voltage Relays

On/Off Relays

|  | Product # | Volts, 60 Hz | Resistive Charge (A) | Supplier | Qty |
| --- | --- | --- | --- | --- | --- |
|  | Without transformer |
|  | RC840 | 120/208/240 | 22 | Honeywell |  |
|  |  | 347 | 18 |  |  |
|  | R841D1036 | 600 | 10 |  |  |
|  | With transformer |
|  | RC840T-120 | 120 | 22 | Honeywell |  |
|  | RC840T-240 | 208/240 | 22 |  |  |
|  | RC840T-347 | 347 | 18 |  |  |
|  | R841C1151 | 600 | 10 |  |  |

NOTE: Not recommended for fast-cycling modulated regulation (more than 6 cycles/hr).

For fast-cycling heating equipment Solid State Relay.

Meant for external installation only. For installation inside heaters, refer to the options table of the concerned product series.

Triac Relays

|  | Product # | Volts, 60 Hz | Input Signal | Resistive Charge (A) | Supplier | Qty |
| --- | --- | --- | --- | --- | --- | --- |
|  | RT850 | 100 to 347 | 4-32VDC, 24VAC | 23 | Honeywell |  |
|  | CCT-25-1-C1 | 208/240/347 | 3-32VDC, 24VAC | 25 | Cristal Controles |  |
|  | CCT-30-1-C2 | 48-600 | 3-32VDC, 24VAC | 30 |  |  |
|  | RT850T-240 | 208/240 | 19.2/24VAC | 23 | Honeywell |  |
|  | RT850T-347 | 347 | 24VAC | 23 |  |  |
|  | CCT-25-1-C2-T | 208/240/277/347 | 14.4/16.6/19.2/24VAC | 25 | Cristal Controles |  |

NOTE: Meant for external installation only. For installation inside heaters, refer to the options table of the concerned product series.

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |