# Series

TH401	Non Programmable Electronic Thermostat

CSA-C828-06 Performance Standard

# Features

Type	-	Non programmable electronic proportional pulsing line voltage thermostat.

Color	-	Standard: white.

Dimension	-	5 in. (127 mm) X 3 3/8 in. (85 mm) X 1 3/16 in. (30 mm).

Voltage	-	120/208/240V, 50/60 Hz.

Rating	-	Maximum resistive load: 10.4A

2500W at 240VAC, 2160W at 208VAC, 1250W at 120VAC.

-	Minimum resistive load: 0.83A

200W at 240VAC, 170W at 208VAC, 100W at 120VAC.

Control	-	5-minute cycle (fan-forced convector) or 15-second cycle (convector).

-	Resolution: 0.5 °C (1 °F).

-	Precision: ± 0.15 °C (0.27 °F) on 15-second cycle.

-	Precision: ± 0.5 °C (1 °F) on 5-minute cycle.

Display range	-	0 °C (32°F) to 50 °C (122 °F).

Setpoint range	-	5 °C (40°F) to 30 °C (85 °F).

Display	-	Digital screen with white LED backlit.

- Display fan-forced convector mode.

-	Choice of temperature display format (°C or °F).

Other feature	-	Temperature setpoints recorded permanently in case of a power outage.

- Ability to set minimum and maximum setpoints.

Installation	-	2-wire thermostat, easy to install.

Application	-	Baseboard heater, radiant ceiling, convector and fan-forced convector.

Warranty	-	3-year warranty against defects.

# Model

| Product # | Description | Volts | Watts | Qty |
| --- | --- | --- | --- | --- |
| TH401 | Non programmable electronic thermostat | 120/208/240 | 1250/2160/2500 |  |

Standard color is white.

# Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |