# Series

HP6000ZB-MA 	Ductless heat pump interface

# Features

# Remote access requires an Internet connection 
and a GT130 smart gateway (not included).

Type	-	Ductless Convectair heat pump interface.

Color	-	Standard: black.

Power supply	-	Connect to the Wi-Fi port on the main board of the indoor unit.

Control	-	Protocol: Zigbee 3.0.

-	Frequency: 2.4 GHz.

-	Transmission power: +20 dBm.

-	Receiver sensitivity: -108 dBm.

- 	Encryption key: AES-128.

Temperature range	-	0 °C (32 °F) to 40 °C (104 °F).

Display	-	Cool, Heat, Dry, Fan and OFF.

-	Adjustment of the orientation of the louvers.

-	Adjustment of the fan intensity.

-	Activation or deactivation of the display.

- Create custom automations.

- Advanced features in Neviweb and Sinopé Smart Systems.

-	Programmation fonctions are available via Neviweb and require a GT130 smart

gateway.

Installation	-	Connect the interface to the USB type Wi-Fi port of the heat pump indoor unit main board.

Application	-	Convectair ductless heat pump1.

Warranty	-	3-year warranty against defects.

# Models

| Product # | Description | Qty |
| --- | --- | --- |
| HP6000ZB-MA1 | Ductless Convectair heat pump interface |  |
| GT130 | Smart gateway that provides remote access to the HP6000ZB-MA |  |

1 Requires the use of the GT130 smart gateway.

### Standard color is black.

# Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact at manufacturer: |  |
| Comments: |

# Footnotes

Available with selected models only.

Require the use of the GT130 smart gateway, an Internet connection and a Zigbee smart thermostat.

# Text boxes

FCC15 Standard Complient

NMB-003 Standard Complient