# Series

OFE-B	First Generation Nortron Electric Furnace

Features

Color	-	Standard: grey.

Voltage	-	208V, 3-phase.

Construction	-	One panel on casing provides access to internal parts.

Fan	-	High quality precision balanced blower for quiet operation and optimal performance.

Motor	-	Standard motor (PSC), permanently lubricated and rubber mounted for maximum vibration and noise reduction.

-  Furnace interlock kit designed to connect the furnace operation with a ventilation fan or a heat recovery ventilator unit (optional).

Heating element	-	Heavy duty, reliable Helical coil nickel-chromium alloy wire provide superior heat transfer with unrestricted air flow.

- Heating elements can be individually replaced.

- High-limit temperature control with automatic reset.

- Elements modulation is done by electro-mechanical sequencers.

Control	-	Heavy duty 24VAC transformer provides power to relays and controls.

-	Easy access built-in breakers with manual reset.

-	“Season Selection” switch: “Mild” or “Cold”.

-	“Recirculation Mode” switch: “On” or “Off”.

-	Compatible with 1 or 2-stage thermostat with or without external unit.

Installation	-	Multi-position installation, sides, back, or bottom air returns.

- Approved for zero clearance installation against combustible surfaces.

Warranty	-	5-year warranty against defects.

Application	-	For cottages, homes or offices, also approved for mobile homes use. May be installed in a basement, closet, crawl space or any unused area or alcove.

# Models 208V with Standard Motor (PSC)

| Product # | Volts (3 ph) 3 wires | kW (BTU/hr) | Amp. including motor | Motor HP | Static Pressure at 0.2" W.C. | Weight | Qty |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Motor Speed1 | Cfm2 | lb | kg |  |
| 83B13-A | 208 | 13.5 (46105) | 42.0 | 1/3 | Medium | 1126 | 105 | 47.6 |  |
| 83B24-A | 208 | 24.0 (81964) | 70.0 | 1/3 | Medium | 1126 | 115 | 52.2 |  |

# Option

| Product # Kit | Description | Qty |
| --- | --- | --- |
| FIK | Furnace Interlock Kit |  |

1 Factory settings.

2 Refer to the installation instructions and owner’s manual for complete air flow tables.

Wall Controls

Compatible with any low voltage thermostat.

# Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |