Series

OCC-RF	Hard-Wired Unit Heater

Features

Color	-	Standard: almond.

Finish	-	Standard: epoxy/polyester powder paint.

Voltage	-	240/208V, 1-phase.

Construction	-	Carrying handle also use as attach point for the wall bracket.

-	6 ft. (2 m) molded electric cable for extra durability.

-	Safely recessed thermostat knob reduces heater size to a minimum.

-	High-limit temperature control with automatic reset.

Fan	-	Open motor.

Note: The open motor is not intended for use in a dusty environment.

-	300 cfm fan.

Heating element	-	Helical coil nickel-chromium alloy wire protected by ceramic insulators.

-	Heating element provides instant heat.

Temperature rise	-	28 °C (51 °F).

Control	-	Built-in thermostat included.

Installation	-	Hard-wired into an electrical junction box (not included).

-	Wall or ceiling mounting using the supplied bracket 	which allow 360° rotation of the 	heater and 	prevent it from tipping over.

Warranty	-	2-year warranty against defects.

Application	-	Workshop, shed, garage.

Models

| Product #1 | Qty | Watts | Volts | Phase | Weight |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | lb | kg |
| OCC4800AMRF-MO-TB6 |  | 4800/3600 | 240/208 | 1 | 16.0 | 7.3 |

1Mounting bracket included.

Standard color is almond.

### Others

| Type | Quantity | Model and description Complementary information | Volts | Phase | Watts | Length mm/in. | Informations Color/installation |
| --- | --- | --- | --- | --- | --- | --- | --- |

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact at Ouellet: |  |
| Comments: |