Series

OCE	European-Style Convector

Features

Color	-	Standard: white, almond.

- Optional (upcharge applicable): metallic silver, bronze, metallic charcoal,

aluminum, semi-gloss black, sand.

-	Custom colors available upon request.

Finish	-	Standard: epoxy/polyester powder paint.

-	Optional: stainless steel (only grilles are painted black).

Voltage	-	240/208V, 50/60 Hz, 1-phase.

Construction	-	20-gauge steel or 22-gauge stainless steel.

-	Warm air outlet that directs the air to the centre of the room.

-	Bar grilles prevent insertion of foreign objects; 
smooth-finish paint is washable and anti-yellowing.

-	High-limit temperature control with automatic reset.

Heating element	-	Quiet aluminum monoblock element.

Watt density	-	OCEH: 850W/ft. (2800W/m)

-	OCEM: 700W/ft. (2320W/m)

-	OCEB: 500W/ft. (1700W/m)

Control	-	Built-in electronic thermostat (-TH models)

or built-in 24V electronic relay (-TRIAC and -TRIACT models).

-	Wall-mounted electronic thermostat (-OTH and -T600 models).

Installation	-	2 in. (51 mm) minimum clearance to ﬂoor.

-	The convector’s wall mounting bracket is connected to the power supply.

-	Simply place the convector on the bracket to make it operational.

Warranty	-	5-year warranty against defects.

(The warranty is valid only if the heater is controlled by a proportional pulsing

electronic thermostat with a cycle of 15 seconds maximum and the junction box must be fixed to the wall with the supplied anchor.)

Application	-	Kitchen, living room, family room, bedroom, bay window, basement.

Models

| Product # | Volts | Watts | Length | Weight |
| --- | --- | --- | --- | --- |
| Non Programmable Built-in Thermostat1 | Qty | Non Programmable Wall-Mounted Thermostat Included2 | Qty | Programmable Wall-Mounted Thermostat Included2 | Qty |  |  | in. | mm | lb | kg |
| OCEH Height: 27” (685 mm) 850W/ft. (2800W/m) |
| OCEH0500-TH |  | OCEH0500-OTH |  | OCEH0500-T600 |  | 240/208 | 500/375 | 10 5/8 | 270 | 14.0 | 6.4 |
| OCEH0750-TH |  | OCEH0750-OTH |  | OCEH0750-T600 |  | 240/208 | 750/563 | 13 1/2 | 344 | 17.0 | 7.7 |
| OCEH1000-TH |  | OCEH1000-OTH |  | OCEH1000-T600 |  | 240/208 | 1000/750 | 16 1/2 | 418 | 19.0 | 8.6 |
| OCEH1250-TH |  | OCEH1250-OTH |  | OCEH1250-T600 |  | 240/208 | 1250/938 | 19 7/16 | 492 | 21.0 | 9.5 |
| OCEH1500-TH |  | OCEH1500-OTH |  | OCEH1500-T600 |  | 240/208 | 1500/1125 | 23 | 584 | 25.0 | 11.4 |
| OCEH1750-TH |  | OCEH1750-OTH |  | OCEH1750-T600 |  | 240/208 | 1750/1313 | 26 1/2 | 674 | 27.0 | 12.3 |
| OCEH2000-TH |  | OCEH2000-OTH |  | OCEH2000-T600 |  | 240/208 | 2000/1500 | 28 1/8 | 714 | 28.0 | 12.7 |
| OCEH2500-TH |  | OCEH2500-OTH |  | OCEH2500-T600 |  | 240/208 | 2500/1875 | 34 | 862 | 33.0 | 15.0 |
| OCEH3000-TH |  | OCEH3000-OTH |  | OCEH3000-T600 |  | 240/208 | 3000/2250 | 41 1/8 | 1044 | 39.0 | 17.7 |
| OCEM Height: 18 1/2” (470 mm) 700W/ft. (2320W/m) |
| OCEM0500-TH |  | OCEM0500-OTH |  | OCEM0500-T600 |  | 240/208 | 500/375 | 13 1/2 | 344 | 13.0 | 5.9 |
| OCEM0750-TH |  | OCEM0750-OTH |  | OCEM0750-T600 |  | 240/208 | 750/563 | 16 1/2 | 418 | 15.0 | 6.8 |
| OCEM1000-TH |  | OCEM1000-OTH |  | OCEM1000-T600 |  | 240/208 | 1000/750 | 19 7/16 | 492 | 16.0 | 7.3 |
| OCEM1250-TH |  | OCEM1250-OTH |  | OCEM1250-T600 |  | 240/208 | 1250/938 | 23 | 584 | 19.0 | 8.6 |
| OCEM1500-TH |  | OCEM1500-OTH |  | OCEM1500-T600 |  | 240/208 | 1500/1125 | 26 1/2 | 674 | 21.0 | 9.5 |
| OCEM1750-TH |  | OCEM1750-OTH |  | OCEM1750-T600 |  | 240/208 | 1750/1313 | 30 5/16 | 769 | 23.0 | 10.5 |
| OCEM2000-TH |  | OCEM2000-OTH |  | OCEM2000-T600 |  | 240/208 | 2000/1500 | 34 | 862 | 25.0 | 11.4 |
| OCEM2500-TH |  | OCEM2500-OTH |  | OCEM2500-T600 |  | 240/208 | 2500/1875 | 41 1/8 | 1044 | 29.0 | 13.2 |
| OCEM3000-TH |  | OCEM3000-OTH |  | OCEM3000-T600 |  | 240/208 | 3000/2250 | 48 3/8 | 1229 | 34.0 | 15.5 |
| OCEB Height: 14” (356 mm) 500W/ft. (1700W/m) |
| OCEB0500-TH |  | OCEB0500-OTH |  | OCEB0500-T600 |  | 240/208 | 500/375 | 19 7/16 | 492 | 13.0 | 5.9 |
| OCEB0750-TH |  | OCEB0750-OTH |  | OCEB0750-T600 |  | 240/208 | 750/563 | 23 | 584 | 15.0 | 6.8 |
| OCEB1000-TH |  | OCEB1000-OTH |  | OCEB1000-T600 |  | 240/208 | 1000/750 | 26 1/2 | 674 | 16.0 | 7.3 |
| OCEB1250-TH |  | OCEB1250-OTH |  | OCEB1250-T600 |  | 240/208 | 1250/938 | 34 | 862 | 20.0 | 9.1 |
| OCEB1500-TH |  | OCEB1500-OTH |  | OCEB1500-T600 |  | 240/208 | 1500/1125 | 36 3/8 | 924 | 22.0 | 10.0 |
| OCEB1750-TH |  | OCEB1750-OTH |  | OCEB1750-T600 |  | 240/208 | 1750/1313 | 41 1/8 | 1044 | 24.0 | 10.9 |
| OCEB2000-TH |  | OCEB2000-OTH |  | OCEB2000-T600 |  | 240/208 | 2000/1500 | 46 7/16 | 1179 | 26.0 | 11.8 |
| OCEB2500-TH |  | OCEB2500-OTH |  | OCEB2500-T600 |  | 240/208 | 2500/1875 | 62 3/16 | 1579 | 35.0 | 15.9 |
| OCEB3000-TH |  | OCEB3000-OTH |  | OCEB3000-T600 |  | 240/208 | 3000/2250 | 69 5/16 | 1760 | 38.0 | 17.3 |

### Options

| Product # Kit | Product # Factory installed* | Description | Qty |
| --- | --- | --- | --- |
| KIT-OCE-AV | - | Tamperproof device |  |
| KIT-OCE-TRIAC-3473 | TRIAC3 | Single-pole electronic relay, coil 24V, without transformer, 15A at 347V max. |  |
| KIT-OCE-TRIAC-347T3 | TRIACT3 | Single-pole electronic relay, coil 24V, with transformer: 15A at 208V, 240V, 347V |  |

* For factory installed options, add the option number to the product number. See the Product Code section inside the front cover.

1 Almond product comes with almond built-in thermostat.

2 Wall-mounted thermostat is white.

3 Do not install a built-in thermostat with these options. Wall-mounted thermostat not included.

Add "BL" for white, "AM" for almond and "SS" for stainless steel. For stainless steel models, only the grille are black painted.

The OCE warranty is valid only if the heater is controlled by a proportional electronic pulsing line thermostat with a cycle of 15 seconds maximum and the junction box must be fixed to the wall with the supplied anchor.

### Others

| Type | Quantity | Model et description Complementary informations | Volts | Phase | Watts | Length mm/in. | Informations Color/installation |
| --- | --- | --- | --- | --- | --- | --- | --- |

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Eectrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |