# Series

OTH2750	Non Programmable Electronic Thermostat

CSA-C828-13 Performance Standard

			ICES-003 Standard Complient

# Features

Type	-	Non programmable electronic proportional pulsing line voltage thermostat.

Color	-	Standard: white.

Voltage	-	120/208/240V, 50/60 Hz.

Rating	-	Maximum load: 11.5A at 120/208/240V.

-	Minimum load: 1.25A at 120/208/240V.

Control	-	10-minute or 15-second cycle.

-	Resolution: 0.5 °C (1 °F).

-	Precision: ± 0.15 °C (0.27 °F) on 15-second cycle.

-	Precision: ± 0.5 °C (0.1 °F) on 10-minute cycle.

Temperature range	-	5 °C (41 °F) to 30 °C (86 °F).

Display	-	Digital screen with white LED backlit.

- Display fan-forced heater mode and keypad lock (when activated).

-	Choice of temperature display format (°C or °F).

Other features	-	Temperature setpoints recorded permanently in case of a power outage.

- Ability to set minimum and maximum setpoints.

- Night light mode for the display LED.

Installation	-	2-wire thermostat, easy to install.

Application	-	Baseboard heater, radiant ceiling, radiant ﬂoor and fan-forced convector.

Warranty	-	3-year warranty against defects.

# Model

| Product # | Description | Volts | Watts | Qty |
| --- | --- | --- | --- | --- |
| OTH2750-A | Non programmable electronic proportional pulsing line thermostat | 120/208/240 | 1380/2390/2750 |  |

Standard color is white.

# Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |