Series

SLIM24 Hyper Heat

Central Heat Pump System and Cased Coil System

Features

Operation mode	- 	Cooling, heating, dehumidifying, fan and auto.

Nominal capacity	-		24000, 36000, 48000, 60000 BTU/hr.

Voltage	-	230/208V, 60 Hz, 1-phase.

Indoor unit	Air Handler

- 	Vertical or horizontal installation.

-	Available with upflow or downflow.

-	Washable filters.

Cased Coil

- Available in four casing dimensions.

- Horizontal or vertical installation.

- Can be matched with third-party gas furnace or blower.

- 24V or 485 communication mode.

Outdoor unit	-	DC motor.

-	Variable speed rotary compressor (INVERTER), with overload protection.

-	Electronic expansion valve for precise control of refrigerant flow.

-	Condenser fins covered with a hydrophilic coating for improved corrosion resistance.

-	Large diameter quiet axial-flow fan for more efficient heat exchange.

-	Multi-hole pan with smart heater to prevent ice formation.

-	Compressor blanket and preheating technology.

-	Installation on aluminum wall bracket or ground stand (optional).

Connection piping	-	Minimum piping length of 10 ft. (3 m).

- Flared connections.

Control 	-	Wireless remote included.

-	Wi-Fi wired wall controller included.

- 	24V thermostat connection available.

-	Set temperature: 16 to 30 °C (61 to 86 °F).

-	Temperature display format: °C or °F.

Warranty	- 10-year basic warranty on parts and 10-year basic warranty on the compressor (labour not included).

- Labour warranty (sold separately) from the 1st to 10th year, on parts and labour with system replacement if the compressor fails.

Application	-	Detached and semi-detached home, commercial building, office building, restaurant.

Features and functions

Models

| Product #1 | Indoor Unit | DEV24H2R19 SHV24H2R20 | DEV36H2R19 SHV36H2R20 | DEV48H2R19 SHV48H2R20 | DEV60H2R19 SHV60H2R20 |
| --- | --- | --- | --- | --- | --- |
|  | Outdoor Unit |  |  |  |  |
| Qty |  |  |  |  |
| Technical Performance |
| Power supply |  | V / Ph / Hz | 230/208 / 1 / 60 |
| Cooling capacity | Nominal | W (BTU/hr) | 7038 (24000) | 10557 (36000) | 13783 (47000) | 16129 (55000) |
|  | Min. – max. | W (BTU/hr) | 3225 - 7918 (11000 - 27000) | 3519 - 13900 (12000 - 47400) | 5279 - 14076 (18000 - 48000) | 4106 - 16422 (14000 - 56000) |
| Heating capacity | Nominal | W (BTU/hr) | 7038 (24000) | 11730 (40000) | 14663 (50000) | 17302 (59000) |
|  | Min. – max. | W (BTU/hr) | 2962 – 9091 (10100 - 31000) | 3226 - 16774 (11000 - 57200) | 3226 - 16129 (11000 - 55000) | 3930 - 20235 (13400 - 69000) |
| SEER / SEER2 | - | 20 / 17.4 | 18 / 16 | 16 / 15.6 | 16.4 / 15.3 |
| HSPF / HSPF2 | - | 12 / 10 | 10.5 / 9.5 | 10 / 9.4 | 10.5 / 9.4 |
| EER | W/W | 13 | 10.5 | 8.5 | 9 |
| COP | W/W | 3 | 1.8 | 1.88 | 1.92 |
| AHRI number | - | 210343158 | 210343156 | 210343157 | 210343159 |
| Indoor Unit (Air Handler) |  |  |  |  |
| Dehumidification | pt/hr (l/hr) | 3.48 (1.98) | 6.1 (3.49) | 4.96 (8.72) | 9.77 (5.55) |
| Air flow volume | T / H / M / L2 | cfm | 824 / 759 / 694 / 629 | 1188 / 1082 / 971 / 865 | 1471 / 1282 / 1094 / 906 | 1806 / 1582 / 1359 / 1135 |
| Sound level | H / M / L2 | dB (A) | 39 / 36 / 33 | 45 / 43 / 41 | 50 / 47 / 43.5 | 51 / 45.5 / 41.5 |
| Fan motor RLA | A | 3 | 4 | 6 | 7 |
| MCOP | A | 15 | 15 | 15 | 15 |
| External Static Pressure (ESP) | Nominal | inH2O | 0.1 | 0.15 | 0.2 | 0.2 |
|  | Range | inH2O | 0 - 0.8 | 0 - 0.8 | 0 - 0.8 | 0 - 0.8 |
| Net weight | lb (kg) | 106 (48) | 129 (59) | 131 (59) | 163 (74) |
| Outdoor Unit |  |  |  |  |
| Air flow volume | cfm | 3000 | 4500 | 4412 | 4500 |
| Sound level | dB (A) | 64 | 64 | 64 | 64 |
| Compressor power input | W | 1945 | 3565 | 3565 | 3770 |
| MCA | A | 20.5 | 41 | 42 | 42 |
| MCOP | A | 35 | 50 | 50 | 60 |
| Compressor RLA | A | 15 | 32 | 33 | 26.2 |
| Fan motor power output | W | 120 | 85 | 85 | 85 |
| Fan motor RLA | A | 1.35 | 1.2 | 1.2 | 1.2 |
| Refrigerant volume (R410A) | oz (g) | 102 (2900) | 165.7 (4700) | 169 (4800) | 169 (4800) |
| Operating ambient temperature | Cooling | °C (°F) | -15 to 50 (5 to 112) |
|  | Heating | °C (°F) | -30 to 24 (-22 to 75) |
| Net weight | lb (kg) | 137 (62) | 227 (103) | 220 (100) | 240 (108) |
| Connection Piping / Refrigerant |
| Pre-charge length | ft. (m) | 25 (7.5) | 25 (7.5) | 25 (7.5) | 25 (7.5) |
| Additional refrigerant charge | oz/ft. (g/m) | 0.69 (65) | 0.69 (65) | 0.69 (65) | 0.69 (65) |
| Liquid pipe outer diameter | in. | 3/8 | 3/8 | 3/8 | 3/8 |
| Gas pipe outer diameter | in. | 3/4 | 3/4 | 3/4 | 7/8 |
| Maximum height between outdoor and indoor units | ft. in. (m) | 82’ (25) | 98’ 5’’ (30) | 98’ 5’’ (30) | 98’ 5’’ (30) |
| Maximum pipe length between outdoor and indoor units | ft. in. (m) | 164’ (50) | 213’ 3’’ (65) | 213’ 3’’ (65) | 213’ 3’’ (65) |

1 1 indoor unit and 1 outdoor unit. Note that each unit is individually packaged.

2 Fan Speeds: (T) Turbo / (H) High / (M) Medium / (L) Low.

Models – Indoor Unit (Cased Coil)

| Product # | Indoor Unit | MAC24H1718E | MAC36H1724E | MAC36H2124E | MAC48H2124E | MAC60H2428E |
| --- | --- | --- | --- | --- | --- | --- |
|  | Outdoor Unit | SHV24H2R20 | SHV36H2R20 | SHV36H2R20 | SHV48H2R20 | SHV60H2R20 |
| Qty |  |  |
| Power supply | V / Ph / Hz | 208/230 / 1 / 60 |
| Capacity | Cooling | BTU/hr | 24000 | 35000 | 36000 | 46000 | 53000 |
|  | Heating | BTU/hr | 25000 | 38000 | 39000 | 51000 | 54000 |
| AHRI number | - | 213160473 | 213160474 | 213160476 | 213160477 | 213160478 |
| Heating at -15 °C (5 °F) | SEER2 | 16.8 | 15.5 | 14.8 | 14.3 | 14.5 |
|  | EER2 BTU/W | 10.7 | 10 | 9.8 | 8.6 | 8.6 |
|  | HSPF2 | 9.5 | 8.6 | 8 | 9 | 8.6 |
|  | Maximum BTU/hr | 20000 | 31600 | 32000 | 40000 | 46500 |
|  | COP W/W | 1.95 | 1.85 | 2 | 1.8 | 1.8 |
| Refrigerant piping | Liquid – Gas | in. | 3/8 - 3/4 | 3/8 - 3/4 | 3/8 - 3/4 | 3/8 - 3/4 | 3/8 - 7/8 |
| Drain pipe diameter | in. | 3/4 | 3/4 | 3/4 | 3/4 | 3/4 |
| Dimension | W x D x H | in. | 17 ½ x 21 x 18 | 17 ½ x 21 x 23 ½ | 21 x 21 x 24 | 21 x 21 x 24 | 24 ½ x 21 x 28 |
|  | W x D x H | mm | 445 x 533 x 457 | 445 x 533 x 599 | 533 x 533 x 609 | 533 x 533 x 609 | 622 x 533 x 711 |
| Net weight | lb (kg) | 43 (19) | 60 (27) | 67 (30) | 67 (30) | 87 (39) |

| Indoor Unit Air Handler | A | B | C | D | E |
| --- | --- | --- | --- | --- | --- |
|  | po | mm | po | mm | po | mm | po | mm | po | mm |
| DEV24H2R19 | 45 | 1143 | 21 | 534 | 17 1/2 | 445 | 15 3/4 | 400 | 10 1/4 | 260 |
| DEV36H2R19 | 49 | 1245 | 21 | 534 | 21 | 534 | 19 1/4 | 490 | 10 1/4 | 260 |
| DEV48H2R19 | 49 | 1245 | 21 | 534 | 21 | 534 | 19 1/4 | 490 | 10 1/4 | 260 |
| DEV60H2R19 | 53 | 1346 | 21 | 534 | 24 1/2 | 622 | 22 7/8 | 580 | 10 1/4 | 260 |
| Indoor Unit Cased Coil | W | D | H |
|  | po | mm | po | mm | po | mm |
| MAC24H1718E | 17 1/2 | 445 | 21 | 533 | 18 | 457 |
| MAC36H1724E | 17 1/2 | 445 | 21 | 533 | 23 1/2 | 599 |
| MAC36H2124E | 21 | 533 | 21 | 533 | 24 | 609 |
| MAC48H2124E | 21 | 533 | 21 | 533 | 24 | 609 |
| MAC60H2428E | 24 1/2 | 622 | 21 | 533 | 28 | 711 |
| Outdoor Unit | W | H | D | A | B |
|  | po | mm | po | mm | po | mm | po | mm | po | mm |
| SHV24H2R20 | 40 1/2 | 1030 | 32 | 810 | 17 7/8 | 455 | 26 1/2 | 673 | 15 7/8 | 404 |
| SHV36H2R20 | 41 1/4 | 1045 | 52 1/2 | 1333 | 18 | 457 | 25 | 634 | 15 7/8 | 404 |
| SHV48H2R20 | 41 1/4 | 1045 | 52 1/2 | 1333 | 18 | 457 | 25 | 634 | 15 7/8 | 404 |
| SHV60H2R20 | 41 1/4 | 1045 | 52 1/2 | 1333 | 18 | 457 | 25 | 634 | 15 7/8 | 404 |

Compatibility table for electrical heating elements

| Electric heater power | 24K BTU | 36K BTU | 48K BTU | 60K BTU |
| --- | --- | --- | --- | --- |
| 5kW | X | X | - | - |
| 8kW | X | X | X | - |
| 10kW | X | X | X | X |
| 15kW | X | X | X | X |
| 20kW | - | X | X | X |
| 25kW | - | - | - | X |

Options

| # Produit Kit | Description | Qty |
| --- | --- | --- |
| Electric auxiliary heat module (for Air Handler only) |
| OTP-EAH-05B-UL | 5kW electric auxiliary heat module |  |
| OTP-EAH-10B-UL | 10KW electric auxiliary heat module |  |
| OTP-EAH-15B-UL | 15kW electric auxiliary heat module |  |
| OTP-EAH-20B-UL | 20kW electric auxiliary heat module |  |

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrical Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact at manufacturer: |  |
| Comments: |