# Series

DS-2C 	Outdoor aerial Mounted Sensor and Controller 
for Heating Cables

# Features

Type	- 	2-in-1 sensor and controller.

- Precipitation sensor on top of unit.

- Temperature sensor below the unit.

Color	- 	Standard : grey.

Power	- 	100-277V, 50/60 Hz.

Rating	- 	30A at 277VAC, 20A at 28VDC.

Construction	-	NEMA 3R rated enclosure, for outdoor installation.

Control	- 	Dry contact relay output, NO (normally open).

Trigger temperature range	- 	1 °C (34 °F) to 6 °C (44 °F).

Display	- 	Power and activation light indicator.

Mode	- 	Control switch on the side of the unit to select operating mode: manual, automatic or standby/reset.

Installation	- 	Screw ¾’’ base conduit hub onto free-standing conduit, or use mounting holes in each corner of the enclosure for wall mounting.

- 	Install controller in a clear space that will receive precipitations.

Note: It is recommended to mount a weatherproof junction box below the controller

to make electrical connections.

Other feature	- 	Adjustment of drying cycle timer (DELAY OFF).

- 	Adjustment of precipitation sensor sensitivity (SENSITIVITY).

Warranty	- 	2-year warranty against defects.

Application	- 	For controlling snow and ice melting cable applications.

- 	Residential driveway, sidewalk, access ramp, underground parking ramp, 
roof and gutter.

Model

| Product # Kit | Description | Amp. | Volts | Qty |
| --- | --- | --- | --- | --- |
| DS-2C | Aerial mounted sensor and controller to detect humidity and temperature | 30A | 277VAC |  |
|  |  | 20A | 28VDC |  |
| DS-8C1 | Aerial mounted controller with a sensor to detect temperature and a sensor to detect humidity with 10 ft. (3 m) cable, 30A, 100V to 277V | - | - |  |
| DS-9C1 | Aerial mounted controller with a sensor to detect temperature and a sensor to detect humidity with 10 ft. (3 m) cable, 2 X 30A, 100V to 277V | - | - |  |
| EX-50 | 50 ft. (15 m) extension kit, with connection fittings for humidity sensor | - | - |  |
| CDP-2 | Interior controller and display for DS products | - | - |  |

1 Requires a ground fault circuit interrupter (GFCI) in the electrical panel.

Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electricial Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |

# Footnotes

Nécessite un détecteur de fuite à la terre (DDFT) au panneau.