# Series

OTH24

# Features

Type	-	Low voltage non programmable electronic thermostat.

Color	-	Standard: white.

Voltage	-	24Vac, 50/60 Hz.

Power	-	1A per output (2 outputs).

Mode	-  First output (main):

A mode: Ambient temperature control.

Note: Floor temperature can be controlled using an external temperature sensor when a floor heating cable is used as the heating source.

F mode: Floor temperature control using an external temperature sensor 
with ability to control the ambient temperature.

-  Second output (auxiliary):

The second output is activated if the first heating system controlled by the first output cannot reach the temperature setpoint.

Control	-	15-second cycle or 5, 10, 15, 20, 25, 30-minute cycle (individually adjustable 
on each output).

- Adjustment of the minimum Time ON and minimum Time OFF on the main output.

Defines the minimum time for which the output can be turned ON or turned OFF (used for heating system with a purge).

- Pump exercise OFF/ON (if set to ON, the thermostat activates its main output 
for 1 minute every 24 hours to prevent pump from seizing).

- Resolution: 0.5 °C (1 °F).

Display	-	Digital display of ambient temperature (°C or °F), heating level indicator and temperature setpoint.

- Backlit - permanent or activated on request.

- Temperature setting recorded permanently.

Temperature range	-	5 °C to 36 °C (41 °F to 97 °F).

Storage Temperature		- -20 °C to 50 °C (-4 °F to 158 °F).

Installation	-	3-wire thermostat (minimum).

Application	-	2 low voltage outputs that can be connected using a 24V relay and a transformer 
to control electric baseboard heaters, convectors, forced-air convectors, electric heating ﬂoors, water pumps and boilers. Note: Select the cycle according to the type of heating.

Warranty	- 3-year warranty against defects.

Model

| Product # | Qty | Volts | Amp. | Description |
| --- | --- | --- | --- | --- |
| OTH24 |  | 24 | 1A | Low voltage non programmable electronic thermostat (2 outputs) |

# Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |

# Text boxes

Low Voltage Non Programable Electronic Thermostat (2 outputs)