# Series

OTH4000-ZB 	Smart thermostat - Zigbee

# Features

# Remote access requires an Internet connection 
and a GT130 smart gateway (not included).

Type	-	Programmable electronic proportional pulsing line voltage smart thermostat.

- Transmitter module: IC: 22394-ZBM1501

Color	-	Standard: white.

Voltage	-	120/208/240V, 60 Hz.

Rating	-	Maximum load: 16.7A at 120/208/240V.

-	Minimum load: 1.25A at 120/208/240V.

Control	-	10-minute cycle (forced-air heater) or 15-second cycle (convector).

-	Resolution: 0.5 °C (1 °F).

-	Precision: ± 0.15 °C (0.27 °F) on 15-second cycle.

-	Precision: ± 0.5 °C (1 °F) on 10-minute cycle.

Temperature range	-	5 °C (41 °F) to 30 °C (86 °F).

Display	-	Digital screen with black backlit.

-	Display forced-air heater mode and keypad lock (when activated).

-	Outside temperature display.

-		Temperature display format (°C or °F) and time format (24h or 12h).

-	Programming features are accessible only through the Neviweb app. 
	The connectivity requires a GT130 smart gateway.

Installation	-	2-wire thermostat, easy to install.

Application	-	Baseboard heater, radiant ceiling, convector and forced-air convector.

Warranty	-	3-year warranty against defects.

# Model

| Product # | Description | Volts | Watts | Qty |
| --- | --- | --- | --- | --- |
| OTH4000-ZB1 | Smart thermostat - Zigbee | 120/208/240 | 2000/3465/4000 |  |
| GT1302 | Smart gateway that provides remote access to the OTH3600-GA-ZB and OTH4000-ZB | - | - |  |

1 Standard color is white.

2 Standard color is black.

# Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact in Ouellet: |  |
| Comments: |

# Text boxes

CSA-C828-13 Performance Standard

ICES-003 Standard Complient