# Series

S1 series	Smart Heat Trace Controller

Features

# Remote access requires an Internet connection.

Type	-		S1-B: Electronic single point line sensing heat trace

c/w Wi-Fi and Ethernet capabilities.

-	S1-A: Same as model S1-B above with added Modbus and BACnet1 capabilities.

Color	-	Standard: white.

Voltage	-	120V- 277V, 50/60 Hz.

Rating	- 	30A resistive.

Construction 	- 	NEMA 4X IP67 enclosure.

Control	- 	Built-in 30 mA to 300 mA GFEP (Default 30 mA).

- 	Dry contact for alarm 1A at 120V or 24VDC, NC (normally closed).

Temperature range 	- -40 ⁰C (-40 ⁰F) to 105 ⁰C (221 ⁰F).

Internet connection	- 	Wi-Fi 802.11 Dual Band 2.4 GHz and 5 GHz and Ethernet (RJ45, Cat 5 or 6).

Display	- 	2.42 in. OLED display, 128 x 64 pixels, menu available in English only.

Accessory included	 - 20 ft. (6 m) lead, 10k ohms thermistor.

Application	-	For controlling heat tracing applications in temperature maintenance

or freeze 	protection applications.

Certification	- UL 1053, UL 60730, CSA C22.2 No.14.

Warranty	-	2-year warranty against defects.

# 1 BACnet IP or MS/TP available via preconfigured SMC gateway, sold separately.

# Models

| Product # | Description | Qty |
| --- | --- | --- |
| S1-A | NEMA 4X IP67 electronic single point line sensing heat trace controller 100-277V, 30A c/w built-in 30 mA GFEP and 20' (6 m) lead, 10k ohms thermistor, Wi-Fi, Ethernet, Modbus and BACnet1 capabilities |  |
| S1-B | NEMA 4X IP67 electronic single point line sensing heat trace controller 100-277V, 30A c/w built-in 30 mA GFEP and 20' (6 m) lead, 10k ohms thermistor, Wi-Fi, Ethernet capabilities |  |
| GATEWAY-PCKG | 24VDC BACnet gateway assembly with power supply NEMA 4X enclosure with 24VDC transformer |  |
| GATEWAY | 24VDC BACnet gateway stand alone |  |

# 1 BACnet IP or MS/TP available via preconfigured SMC gateway, sold separately.

# Specifications may change without prior notice

| Project: | Approval Information |
| --- | --- |
| Consultant Engineer: |  |
| Electrician Contractor: |  |
| Distributor: |  |
| Date: |  |
| Contact at manufacturer: |  |
| Comments: |